## Slide 1: Slice2mesh: meshing sliced data for the simulation of AM processes
M. Livesu
D. Cabiddu
M. Attene

## Slide 2
Motivation
  Simulation of AM processes is a mean to
PREVENT FAILURES
PREDICT QUALITY
    Cost: a failure is a waste of time and material
    Fidelity: objects should be design compliant

## Slide 3
DYNAMIC
DOMAIN
A meshing perspective
  Simulating AM requires a discrete representation of the domain
  Three major requirements
LOCAL
REFINEMENT
SUPPORT
SYNTHESIS
STANDARD TECHNIQUES FALL SHORT!

## Slide 4
What input?
PART
ORIENTATION
SUPPORT
STRUCTURES
SLICING
MACHINE
TOOLPATH
M 270
DESKTOP
PART
ORIENTATION
SUPPORT
STRUCTURES
SLICING
INDUSTRIAL

## Slide 5
Anatomy of a slice
  Objects encoded as piece-wise linear open/closed curves
    Outer perimeter is a CCW closed curve
    Holes are CW closed curves
    Supports are open curves

## Slide 6
Slice2Mesh
  Transform slices into volumetric meshes
SLICE CONFORMING (OUTSIDE)
SLICE CONFORMING (INSIDE)

## Slide 7
Basic idea
Extrude each slice along the build direction
Merge adjacent slices in a conforming way
Tetmesh the resulting PLC to produce a tetrahedral mesh

## Slide 8
Basic idea
NON
CONFORMING
Extrude each slice along the build direction
Merge adjacent slices in a conforming way
Tetmesh the resulting PLC to produce a tetrahedral mesh

## Slide 9
Basic idea
CONFORMING
Extrude each slice along the build direction
Merge adjacent slices in a conforming way
Tetmesh the resulting PLC to produce a tetrahedral mesh

## Slide 10
Basic idea
OUTER
BOUNDARY
INNER SLICES
NON
MANIFOLD
EDGES
Extrude each slice along the build direction
Merge adjacent slices in a conforming way
Tetmesh the resulting PLC to produce a tetrahedral mesh
  Use standard tools (i.e. Tetgen)
  Tetrahedra do not span multiple slices
  Filtering tets reproduces the temporal evolution of the domain

## Slide 11
For each edge e of each slice si
  Create a copy e’ and lift it to si+1
  Intersect e’ with all the edges in si+1
Triangulate the resulting “quads”
Run Tetgen on the resulting PLC
s0
s1
s2
Input: a set of slices (s0,…, sn )
Output: a simulation ready tetrahedral mesh
Lifting Algorithm

## Slide 12
Support structures
  Support structures are 1D open curves replicated at each slice
  We use curve thickening. Thickening radius matches
    The filament cross-section in FDM
    The Laser beam in SLS/SLM
    …
Boost Polygon Library (buffer)

## Slide 13
Support structures
  Support structures are 1D open curves replicated at each slice
  We use curve thickening. Thickening radius matches
    The filament cross-section in FDM
    The Laser beam in SLS/SLM
    …
Boost Polygon Library (buffer)

## Slide 14
Considerations
  Working in slice space offers a number of advantages
    Complexity of 3D objects disappears: everything is 2D!
    Complex of supports/infills disappears as well: everything is 2D!

## Slide 15
Considerations
  Working in slice space offers a number of advantages
    Complexity of 3D objects disappears: everything is 2D!
    Complex of supports/infills disappears as well: everything is 2D!
    Domain simplification for faster simulations is trivial (filter slices!)
~80 slices
~170K tetrahedra
~40 slices
~35K tetrahedra

## Slide 16
Limitations
  More an academic prototype than a professional meshing tool
s0
s1
s0
s1

## Slide 17
Limitations
  More an academic prototype than a professional meshing tool

## Slide 18
MESHING TO SIMULATE
3D PRINTING
NEW CHALLENGES, STANDARD TECHNIQUES FALL SHORT
SLICE2MESH
A FIRST (RATHER TRIVIAL) SOLUTION
https://github.com/mlivesu/slice2mesh
Conclusions
LIMITATIONS
- ROBUSTNESS
- OVER REFINEMENT
FUTURE WORKS
- VALIDATE MESHES IN REAL SIMULATIONS
- MESH ALONG TOOLPATHS
- USE HEXAHEDRA or PRISMS

## Slide 19
THANK YOU!